Description
industrial-grade, Bluetooth serial module Bluetooth module, from one of BC04
Description
The BLK-MD-BC04-B is currently on the market the most powerful serial Bluetooth module, its to adopt Blue2.0, to support the master-slave mode, support for hardware / software settings to the master and slave modes support up to 29 AT commands and nine automatic feedback instruction, support baud rate 1200-1382400.
Features
1) Support for Bluetooth Specification V2.1 + EDR
2) Support for hardware / software to set the master and slave modes
3) AT command set control parameters for the module and issued an order
4) Working status indicator: connection, connection status signal output, ease of MCU status tracking mold block
5) Ideal for embedded wireless serial transmission alternative
6) Onboard efficient antenna
7) Support the connection of seven from the device
8) 3.3V power supply
Product Application
1) Bluetooth wireless data transmission
2) POS systems, wireless keyboard, mouse
3) Automated data transfer; banking system
4) Remote control and monitoring
5) Automotive testing equipment
6) Bluetooth remote control toys
7) Wireless data collection
8) Building automation and Hugh, security, powerhouse equipment wireless monitor, access control systems
9) Government street lights energy-saving equipment
10) Traffic, underground location, alarm
11) Wireless LED display systems
12) Television interactive programming voting equipment
13) Bluetooth Printer
14) Bluetooth joystick, Bluetooth game controller
15) Smart home, industrial control
16) Automated data acquisition system
Master and slave settings and other configuration
1, the module master-slave mode is settable
BLK-MD-BC04-B Bluetooth module supports both hardware / software to set the main model, specific methods are as follows:

PI0 (4) - hardware / software master and slave port settings: low (or floating) master-slave mode, set 3.3V high for the software to set the main settings for the hardware slave mode; If you choose the hardware setup master-slave mode can be PIO (5) settings; If you select the software to set the master-slave mode, you can query and set of AT commands, the method-specific reference "BLK-MD-BC04
B Bluetooth module AT command Help

The PIO (5) - Hardware main set port: 3.3V high set mode, the ground (or vacant) is set to slave mode.
2, the status indicator LEDs: the PIO (1)
Used to indicate which the status of the Bluetooth module, the LED light flashes with the Bluetooth module state corresponds to the following table:

3, the host interrupt indicator LED: the PIO (2)
Used to indicate the host to interrupt it or not, the connection status is high, other state low.
4, clear the memory or Restore Defaults button: PIO (3)
This button is a multi-function key has a memory clear (short press), restore the default value (long press 3s) are two different functions; memory clear is to remove the Bluetooth address code of the last memory module; restore the default value is early recovery module The initial default values.
Product Specifications
1) Bluetooth protocol Bluetooth Specification v2.1 + EDR
2) USB protocol USB v1.1/2.0
3) Frequency band for the ISM 2.4GHz
4) Modulation GFSK (Gaussian Frequency Shift Keying)
5) Transmit power ? 4dBm, Class 2
6) Sensitivity ?-84dBm at 0.1% BER
7) Rate for Asynchronous: 2.1Mbps (Max) / 160 kbps,
8) Synchronous: 1Mbps/1Mbps
9) Authentication and encryption of security features
10)  Support profiles, the SPP (the master & slave)
11) Power supply +3.3 VDC, 50mA
12) Operating temperature -20 ~ +55 Centigrade
13) Size 26.7mm x 13mm x 2.2 mm
14) The current firmware has been upgraded to the latest version: serial port default baud rate is 9600, the pair: 1234, the default name: BOLUTEK