Description
Item Name Bluetooth UART RS232 serial converter Module
Operating Frequency Band: 2.4GHz unlicensed ISM band
Bluetooth Specification: V2.0+EDR
Output Power Class: Class 2
Operating Voltage: 3.3V
Host Interface: USB/UART
Audio Interface: None
Flash Memory Size: 8Mbit
Dimensions: 27.2mm x 12.8mm x 2.5mm
Net Weight: 9.6 g / 0.3 oz
Key Features
*support Master and Slave mode, modify by AT commander
1. CSR Bluetooth Chip Solution
2. Bluetooth Spec v2.0+EDR Compliant
3. Enhanced Data Rate (EDR) compliant with V2.0.E.2 of specification for both 2Mbps and 3Mbps modulation modes
4. Full Speed Bluetooth Operation with Full Piconet Support and Scatternet Support
5. Increadible samll size with 3.3V input, and RoHS Compliant
6. UART interface and with baudrate setup function
7. Support for 8Mbit External Flash Onboard
8. Support for 802.11Co-Existence
Product Description
The Bluetooth UART RS232 serial Converter Module can easily transfer the UART data through the wireless Bluetooth, without complex PCB layout or deep knowledge in the Bluetooth software stack, you can combine this bluetooth module with your system:
* MCU, ARM or DSP systems.
* SOC systems.
* Personal Digital Assistants (PDAs)
* Computer Accessories
* Other systems your want to use under bluetooth functions.

[Hardware]
1. CSR solution, Bluetooth V2.0 protocol
2. support AT commander
3. support Master and Slave mode, modify by AT commander
4. support 1200-115200 baudrate
5. 3.3V single supply
6. Size: core module: 28mm*15mm*2.35mm, whole module:35.33mm*19.6mm*3.7mm
7. current: 30mA MAX
8. can be used with all MCU by UART port
9. 2 indicator lights
Pin Functions:
1) TX
2) RX
3) CTS
4) RTS
5) RCM CLK
6) PCM OUT
7) PCM IN
8) PCM SYNC
9) AI00
10)  AI01
11)  RESET
12)  3.3V
13)  GND
14)  NC
15)  USB D-
16)  CSB
17)  MOSI
18)  MISO
19)  CLK
20)  USB D+
21)  GND
22)  GND
23)  PI01
24)  PI02
25)  PI03
26)  PI04
27)  PI05
28)  PI06
29)  PI07
30)  PI08
31)  PI09
32)  PI010
33)  PI011